## Slide 1
RENEWABLE ENERGY INTEGRATION
Grid Stability & Cross Country Connectivity
Sanjoy Mukherjee
Executive Director (Distribution Technical)
CESC LIMITED

## Slide 2
236 GW
Thermal
47 GW
Hydro
* RE capacity today 114 GW (28% of installed capacity); as on 30.06.2022
Power Sector in India at a Glance
399 GW
7 GW
Nuclear
110 GW
RES*
Solar: 54 GW; Wind: 40 GW
Others: 16 GW
Installed Capacity
as on Mar’22
Major capacity expansion of greenfield solar capacity
2014
14
2022
28
Chart: 
| FY14 | FY15 | FY16 | FY17 | FY18 | FY19 | FY20 | FY21 | FY22
Thermal | 168.255 | 188.8978 | 210.675 | 218.3299 | 222.9066 | 226.2793 | 230.5996 | 234.7282 | 236.1087
Nuclear | 4.78 | 5.78 | 5.78 | 6.78 | 6.78 | 6.78 | 6.78 | 6.78 | 6.78
Hydro | 40.5314 | 41.2674 | 42.7834 | 44.4784 | 45.2934 | 45.3992 | 45.6992 | 46.2092 | 46.7225
Solar | 2.6319 | 3.744 | 6.7629 | 12.2888 | 21.6515 | 28.1807 | 34.6278 | 40.0854 | 53.9965
Wind | 21.0426 | 23.3544 | 26.7774 | 32.2798 | 34.046 | 35.626 | 37.6938 | 39.2471 | 40.3576
Others | 11.3135 | 11.8608 | 12.3838 | 12.6756 | 13.3249 | 13.8349 | 14.7061 | 15.1014 | 15.5313
Percentage Share | 0.14077 | 0.14172 | 0.15049 | 0.17515 | 0.20065 | 0.21803 | 0.23514 | 0.24711 | 0.27506
Evolving Generation Capacity mix (GW)
*All in GW
Source: https://cea.nic.in/installed-capacity-report/?lang=en
Chart: 
| Thermal | Nuclear | Hydro | RES
FY22 | 236.1087 | 6.78 | 46.7225 | 109.8854
Thermal, 59%
RES, 28%
Hydro, 12%
Nuclear, 2%
Distributed generation with coal capacity growth slowing down and solar PV and wind ramping up, the share of variable renewables in installed capacity has doubled since 2014.
Largely coal-based capacity expansion to meet the growing energy demand in India

## Slide 3
RE Target
Total RE Target by 2022
175 GW
Solar
100 GW
Wind
60 GW
Small Hydro
5 GW
Bio-mass
10 GW
2022
Total RE Target 175 GW
2030
Total RE Target 500 GW
India's non-fossil energy capacity to reach 500 GW by 2030.
India will meet 50 per cent of its energy requirements with renewable energy by 2030.
India’s RE ambitions
By 2070, India will achieve the target of net zero emissions.
*Out of 100 GW solar capacity target, 40 GW is from rooftop
Source: https://economictimes.indiatimes.com/industry/renewables/india-keeps-renewables-target-flexible-goal-of-500-gw-green-energy-by-2030-dropped/articleshow/93357477.cms?from=mdr
51%
Solar and wind will make up
2030
31%
drop in reliance on coal
820 GW
CEA Projection by 2030
https://powermin.gov.in/sites/default/files/uploads/MOP_Annual_Report_Eng_2021-22.pdf

## Slide 4
Transmission Planning for 500 MW of non-fossil fuel by 2030
Waiver of ISTS Transmission Charges and Losses for Solar & Wind Power
Pan-India market-based Renewable Energy Certificate (REC) Mechanism to promote renewable energy
Issuance of Renewable Purchase Obligations (RPO) Trajectory FY23 : 24.61% to FY30: 43.33%
Deepening of spot markets: Introduction of Green Day Ahead Market (GDAM) & Green Term Ahead Market (GTAM) in Power Exchanges
Procurement of Round The Clock (RTC) Power from Renewable Projects through Tariff Based Competitive Bidding
Scheme for flexibility in Generation and Scheduling of Thermal/ Hydro Power Stations through bundling with Renewable Energy and Storage Power
Green Energy Open Access >100 kW
Measures to Promote Growth of Renewable Energy

## Slide 5
Source: CEA report on ‘Flexible operation of thermal power plant for integration of RE generation’,2019
Alternative scenario – installed capacity (2030): 820 GW
Chart: 
| Thermal | Nuclear | Hydro | RES
FY30 | 244 | 7 | 69 | 500
Thermal, 244
RES, 500
Hydro, 69
Nuclear, 7
RE Scenario & Projected Load Curve
As overall electricity demand and renewables’ share of India’s generation grows, the ramping need between 17:00 (5pm) and 19:00 (7pm) is expected to increase from ~13 GW in 2017 to over 75 GW in 2030.
0 2 4 6 8 10
12 14 16 18 20 22
16 17 18 19 20
Hour of the day
150GW
200GW
250GW
~75 GW
2030
Total electricity Demand
Net electricity Demand
The present capacity of thermal sources can provide 13 GW/min ramp-up capacity. Hydro generation can provide a high ramp-up (25 GW/min but generation will be subject to weather and monthly patterns
In order to meet its net demand, India will need a ramp-up of 55−60 GW in 6 hours with RE penetration of 175 GW
All India demand and net demand (for a typical day) − GW

## Slide 6
Challenges
Recommendation
RE Grid Integration challenges & Recommendation
Meeting net load (high ramp-up/ramp-down)
Meeting variability and intermittency; Maintaining Grid Stability
Challenges :
Recommendation
Additional flexible source addition (pumped storage, battery, hydro, demand side management)
Deeper short-term markets and ancillary markets
Strong enforcement of regulations like DSM regulations
Co-ordinated scheduling and despatch
Maintaining Minimum Load Operation of conventional generators
Challenges :
Recommendation
Joint operation of solar and hydro energies because of their complementary nature
Flexible power from hydro and gas, with both sources generating less during the day and more during peak hours compared to the present trend of generation
Flexible power from pump/battery storage and coal to provide peak support
Existing power market design (High long-term access [LTA]/PPA, no mature market for ancillary, short-term or capacity market)
Challenges :
Recommendation
Improve volume, liquidity and flexibility of the power market
Design of new power market structure with key characteristics such as:
  Retail competition
  compulsory participation in exchange
  implementation of capacity market
  competitive ancillary market
Power Quality Issues like Voltage Sag & Swell, Harmonics, Phase Unbalancing
Challenges :
Recommendation
Uninterruptible Power Supply (UPS)
Ferro resonant transformers
Dip correctors
Energy storage technologies
Battery Energy Storage Systems:
GoI planning to float tenders for sourcing 4000 MWh battery storage, power & renewable energy
*Out of 100 GW solar capacity target, 40 GW is from rooftop

## Slide 7
Towards a 100% Renewable Energy Future
Enhance security of supply, by increasing the diversification of energy sources
Cheap RES production over long transmission lines
RES Availability Round the Clock & Optimization of RE resources
Smoothing out electricity Supply and Demand
Interconnecting more grid increases reliability in supply
Interconnections decrease the need for balancing power
Less need for bulk storage
Boost developing economies and reduce their GHG emissions
Sources: S. Chatzivasileiadis, D. Ernst, G. Andersson, The Global Grid, Renewable Energy, 2013
Global Grid
One Sun One World One Grid (OSOWOG)
“We have a dream called One World, One Sun One Grid. We can generate round the clock electricity from the sun as it sets in one part of the world but rises in another part. The sun never sets for the entire earth.”
India’s Vision
http://theglobalgrid.info/presentations/Chatzivasileiadis_theglobalgrid.pdf
Cross Country Connectivity
Benefits

## Slide 8
Cross Country Connectivity
The Global Grid is just a few years away
1866: First successful submarine cable
1901: Global Telegraphy Network
Now: An Intensive Undersea Internet World

## Slide 9
Source:
https://blog.forumias.com/discom-sector-in-india-challenges-solutions-explained-pointwise/#:~:text=High%20AT%26C%20losses%3A%20The%20precarious,subsidy%20support%20from%20state%20governments.
Cross Country Connectivity
Key Challenges
A Global Electricity Grid is technically feasible and can potentially be economically competitive
http://theglobalgrid.info/presentations/Chatzivasileiadis_theglobalgrid.pdf
Investments
Regulatory
Operation
Technical

## Slide 10
Thank You!!