## Slide 1
30th Nov 2021
Ecological Sustainability in Industrial Region
Haldia Edition
Exide Industries Ltd. Haldia
30TH NOV’21

## Slide 2
For more than six decades, Exide has been one of India's most reliable brands, enjoying unrivalled reputation and recall. Our constant emphasis on innovation, extensive geographic footprint, strong relationship with marquee clients and steady technology upgradations with global business partners have made us a distinct frontrunner in the lead-acid storage batteries space for both automotive and industrial applications
EXIDE INDUSTRIES LTD.
A leader in packaged power technology, EIL today is India's largest storage battery company with widest range of both conventional flooded as well as latest VRLA batteries. Apart from serving the domestic market the company exports batteries which have captured niches in South East Asian and European markets.
LEADERSHIP

## Slide 3
Locational Advantage
Multi-locational facilities evade supply risks, ensuring delivery
Strategically located near markets
Proximity to ports facilitate cost-efficient exports and imports
Legend
ISO 9001:2015
ISO 14001:2015
IATF 16949-2016
OHSAS 18001:2007
MANUFACTURING CAPACITIES
GEOGRAPHIC PRESENCE

## Slide 4
Vision
To become a Global Power House respected by customers and preferred by investors, known for innovative products and solutions.
To outperform at market exceeding expectations of customers and shareholders through the accelerated evolution of people, processes and technologies in its journey towards excellence.
Mission

## Slide 5
Leadership
Integrity
People Development and Involvement
Agility
Passion for innovation and Technology
Channel Partner Relationship
Striving for Excellence
Customer Orientation
Management by Processes and Facts
Responsible Corporate Citizenship
Core Values

## Slide 6
There are many Large , Medium & Small scale industries in and around Haldia
Introduction Of Haldia
Exide Haldia
Surrounded by several Benchmark Companies
KoPT

## Slide 7
Operation started | Mar ’80 |  |  | Employees | 700
Plant Area | 41 Acres +19.4 Acres |  |  |  | 
 |  |  |  | Product range | Automotive Industrial
Floor space | 59,950 m2 |  |  |  | 
Green Area | 42,627 m2 |  |  |  | 
Admin
Building
Automotive
Factory
Industrial Factory
Traction Factory
Exide - Haldia at a Glance
N
Alpha
Project
Auto Charging & Dispatch
Newly acquired
19.4 Acre land

## Slide 8
Plant Capacity
AUTOMOTIVE
5.3 MILLION BATTERIES / YEAR
INDUSTRIAL
2028 MILLION AMPERE HOUR/YEAR
(2.1 Million 12V Batteries + 1.2 Million 2V Cells)

## Slide 10
ECOLOGICAL SUSTAINIBILITY
It is basically everything connected to the Earths Ecosystem.
Amongst other things, ecological sustainability relates to the functioning of the Earth's biogeochemical system, which includes the following:
Water (pollutants, groundwater levels, salinity, temperature, alien species)
Air (pollutants, particles, ozone layer, climate system, noise)
Land (pollutants, erosion, land use, alien species)
Biodiversity (species and habitats (natural habitats), GMOs)
Ecosystem services (e.g. pollination, photosynthesis, water purification, climate control)
It includes Human health due to the over all Environment pollution in the Industrial Zone.

## Slide 11
EXIDE
Committed to serve with cleaner safer and sustainable world.
SUSTAINABILITY POLICY
HR POLICY
BIODIRVERSITY POLICY
EHS POLICY
PRODUCT RESPOSIBILITY POLICY

## Slide 12: Our Focus
Exide is focussed on sustainability of
Economy
Society
Environment
Increasing ratio of population and industrialization have a lot of negative impacts on the human and other living systems. Utilization of natural resources abruptly and other non-enviro-friendly activities should be controlled and there is need to put Environment sustainability plan in place by all Industries to handover a cleaner and safer world to our upcoming generation

## Slide 13
Commitment towards protecting
Environment
Occupational Health
And safety of people
Focus on continual improvement and sustain the standards, complying all statutory requirements.
Environment Health and Safety Policy

## Slide 14
Battery Manufacturing Process

## Slide 15: Initiative towards Ecological Sustainability
Protect Environment
  Soil
  Air
  Water
  Waste management
  Reduction in Energy
  Sustainable source of ingredients on procurement
  Strong Vendor policy on recycling of used battery.
  Corporate Social Responsibility

## Slide 16: TO REDUCE PROCESS WATER

## Slide 17
+VE TANK
SUMP PIT
Positive Pasting M/c
- VE TANK
Negative Pasting M/c
SUMP PIT
To Homogeneous Tank
To Homogeneous Tank
AOD Pump
AOD Pump
DM water line for make up
Over flow
PASTE RECOVERY SYSTEM
TO DRAIN
BEFORE
DRAIN
+VE TANK
SUMP PIT
Positive Pasting M/c
SS Tank for +VE water
SS Tank for -VE water
- VE TANK
Negative Pasting M/c
SUMP PIT
To Homogeneous Tank
To Homogeneous Tank
AOD Pump
AOD Pump
DM water line for make up
Over flow
AFTER
Overflow
TO BE USED IN:
a) Reuse in pasting M/C
b) In machine washing
c) In Paste Mixing
Initiatives to reduce process water

## Slide 18
Cooling Tower
J/F Tank
Reservoir
Over flow
Over flow to Drain
Pump
BEFORE
Cooling Tower
J/F Tank
Reservoir
Storage Tank
Over flow
V
As make up water
TO BE USED IN : Recycle back to the system
BENEFIT : RAW WATER = 40 KL/DAY
Pump
AFTER
Initiatives to reduce process water

## Slide 19
Re-use of RO waste water.
Use for Gardening
Use in E.T.P for Lime slurry preparation
Re-use of Lagoon discharge water for battery charging process
CONTINUOUS ACTIVITY-REUSE OF WASTE WATER FROM RO PLANT AND LAGOON DISCHARGE

## Slide 20
REDUCTION OF PROCESS WATER THROUGH TECHNOLOGY UPGRADATION
Conversion of dry filling to wet filling for positive plates
Conversion of conventional water bath charging to re-circulation charging
Dry Filling
Acid Pickling
Washing
Drying
Finished Plates to Assembly
Generation of fines
Generation of huge sludge
Wet Filling
Drying
Finished Plates to Assembly
Generation of fines eliminated
Generation of sludge eliminated
X
X

## Slide 21
ADVANTAGES
Generation of fines eliminated
Minimum sludge generation due to
elimination of pickling
DRY OXIDE FILLING
WET FILLING
OXIDE FILLING PROCESS CHANGE IN TUBULAR PLATES FOR INDUSTRIAL

## Slide 22
ADVANTAGES
Availability of optimum specific gravity acid for
formation of positive & negative plates enables
low AH I/P during charging
Use of chilled acid enables charging to takes place at
50 % lower time
WATER BATH CHARGING
RECIRCULATION CHARGING
BATTERY CHARGING PROCESS- WATER BATH CHARGING TO RECIRCULATION CHARGING

## Slide 23
Chart: Raw Water(KL/MT of Lead
| 2016-17 | 2017-18 | 2018-19 | 2019-20 | 2020-21 | 2021-22(YTD Sept) | 2022-23 | 2023-24 | 2024-25 | Raw Water(KL)/MT of Lead
 | 5.7 | 5.72 | 5.19 | 4.58 | 4.43 | 4.82 | 4.2085 | 3.9981 | 3.7982
WATER CONSUMPTION REPORT
Chart: 
| 15-16 | 16-17 | 17-18 | 18-19 | 19-20 | 20-21 | 21-22 YTD OCT'21
Rs. Crores | 921 | 1229 | 1355 | 1563 | 1633.92 | 1590
April'11 | 1122.32
Chart: 
| 15-16 | 16-17 | 17-18 | 18-19 | 19-20 | 20-21 | 21-22 YTD OCT'21
AUTOMOTIVE PRODUCTION (Lac Plates) | 1175 | 1265 | 1349 | 1460 | 1427 | 1548
YTD Apr '13 | 948
Automotive Production(Million Ah)
Prod. Volume Increase from 2016-17 to 2020-21 - 50%
Raw Water Cons. Reduction - 29%
INDUSTRIAL & AUTOMOTIVE

## Slide 24
Raw Water(KL)/MT of Lead |  |  |  |  |  |  |  | 
2016-17 | 2017-18 | 2018-19 | 2019-20 | 2020-21 | 2021-22(YTD Sept) | 2022-23 | 2023-24 | 2024-25
5.70 | 5.72 | 5.19 | 4.58 | 4.43 | 4.82 | 4.21 | 4.00 | 3.80
DM Water(KL)/MT of Lead |  |  |  |  |  |  |  | 
2016-17 | 2017-18 | 2018-19 | 2019-20 | 2020-21 | 2021-22(YTD Sept) | 2022-23 | 2023-24 | 2024-25
1.48 | 1.40 | 1.35 | 1.80 | 1.48 | 1.57 | 1.49 | 1.42 | 1.35
Chart: DM Water(KL)/MT of Lead
| 2016-17 | 2017-18 | 2018-19 | 2019-20 | 2020-21 | 2021-22(YTD Sept) | 2022-23 | 2023-24 | 2024-25
 | 1.48 | 1.4 | 1.35 | 1.8 | 1.48 | 1.57 | 1.4915 | 1.4169 | 1.3461
WATER CONSUMPTION REPORT
28% Redn.
16% Redn.

## Slide 25
S.T.-1
Red Slurry
S.T.-2
Red Slurry
S.T.-3
Red Slurry
Pump On
ETP DRAIN
P
BEFORE
No process for recovering the Slurry and Spill out DM after decanting .
SLURRY MIXING & PREPARATION
PLANT
R.T.-1
R.T.-2
R.T.-3
Red Slurry
P
P
MAIN DM LINE
P
L1
L1
MIXING TANK
P
Red Slurry
P
P
P
P
P
P
M/C
Red Slurry
Red Slurry
Converted in closed loop system and scrap is reduced
Benefit :
6 KL/ Day
TO BE USED IN:
Slurry Mixing
AFTER
Initially process water directly goes to ETP. After treatment more sludge generated.
Initiative taken to reuse of water after recovery from process water.
Which helps to reduce 6 Kl of water savings every day. Simultaneously reduction in ETP treatment and reduction in sludge generation.
PROJECTS ON WASTE & SLUDGE REDUCTION

## Slide 26
Chart: Elec. Energy(KWH/MT of Lead
| 2016-17 | 2017-18 | 2018-19 | 2019-20 | 2020-21 | 2021-22(YTD Sept) | 2022-23 | 2023-24 | 2024-25 | Energy(KWH)/MT of Lead
 | 1501.42 | 1429.92 | 1324 | 1283.03 | 1152.21 | 1104.52 | 1049.294 | 996.8293 | 946.9878
ENERGY CONSUMPTION REPORT
ELECTRICAL LOAD DEMAND MONITERING THORUGH VARIOUS ENERGY MANAGEMENT PROJECT
36% Redn

## Slide 27
BDL | → | Below detectable level | 
ND | → | Not Done | 
Monitoring of outside discharge water -pH, Pb, COD, BOD & TSS |  |  |  |  |  |  |  | 
Sl. NO | Location | Parameters | Month |  |  |  |  | 
 |  |  | Aug-2021 |  | Sep-2021 |  | Oct-2021 | 
1 | Lagoon Discharge | pH (6.5-8.5) | 7.3 | 7.3 | 7.36 | 6.9 | 7.53 | 7.1
 |  | Pb(0.1mg/lt) | 0.027 | 0.056 | 0.027 | 0.073 | 0.024 | 0.054
 |  | COD(250 mg/lt) | 8.5 | - | 4 | - | 9.1 | -
 |  | BOD(30mg/lt) | <2 | - | <2 | - | <2 | -
 |  | TSS(50 mg/lt) | 11 | - | 14 | - | 10 | -
2 | Traction Discharge | pH (6.5-8.5) | 7.53 | 7 | 7.28 | 7.1 | 8.35 | 6.7
 |  | Pb(0.1mg/lt) | 0.02 | 0.032 | 0.022 | 0.061 | 0.019 | 0.073
 |  | COD(250 mg/lt) | 4.3 | - | 4 | - | 9.1 | -
 |  | BOD(30mg/lt) | <2 | - | <2 | - | <2 | -
 |  | TSS(50 mg/lt) | 9 | - | 11 | - | 10 | -
CONFORMATION TO ENVIRONMENTAL NORMS
Schedule:
Self Engaged outside Agency-Weekly
Internal Lab & on-line monitoring system

## Slide 28
Stack | Apr-21 | Jun-21 | Aug-21 | Sep-21 | Oct-21
Alloy - Blending Pot(Burner ) |  |  |  |  | 
Alloy - Blending Pot |  |  |  |  | 
Reaction Pot (Auto) |  |  |  |  | 
Grid Casting Pot (Auto ) |  |  | 0.58 |  | 
Li Shan Oxide Mill 12MT (Auto) | 3.99/ BDL |  | 0.33 |  | 
Assembly (Auto ) |  |  |  |  | 
Pasting (Auto ) | 7.41/BDL |  |  |  | 
Jarformation (Scrubber No.1) |  |  |  |  | 
Jarformation (Scrubber No.2) |  |  |  |  | 
Oxide Ball Mill (Auto) | 8.16/BDL |  |  |  | 
Oxide Ball Mill (Auto) | 4.79/BDL |  | 1.77 |  | 
Grid Casting ( Indl) |  |  |  |  | 
Pasting ( Indl) |  |  |  |  | 
Spine Casting (Indl) |  | 18/5.2 | 0.70 |  | 14/6.8
Ball Mill (Indl) | 5.75/BDL |  | 0.78 |  | 
Assembly (Indl) |  | 19/6.2 |  |  | 12/7.9
Exide filling | 14.5/BDL |  |  |  | 
Rotary Shaker ( Indl) |  |  |  |  | 
Casting ( Traction) |  |  |  |  | 
Pasting( Traction) |  | 20/6.1 | 8.84 |  | 
Ball Mill ( Traction) | 6.75/BDL |  |  |  | 
Assembly(Traction) |  | 15/5.9 |  |  | 
Cell charging (Traction) |  |  |  |  | 
Assembly ( Auto) |  |  |  |  | 
Charging (Indl) |  |  |  |  | 
Strip Caster |  | 19/6.2 |  |  | 20/7.1
2 nos Recator | 0.67/BDL | 17/7.1 | 0.45 |  | 18/7.4
2 nos Paste mixer |  |  |  |  | 
Assembly (Automotive Alpha) |  | 18/6.5 |  |  | 20/7.2
DG set (Auto. Alpha) |  | 70 |  |  | 50
Alpha charging |  |  |  |  | 
Oxide Filling (Sungwoon)(Indl) |  |  |  |  | 
Ball Mill (Indl) | 4.8/BDL |  | 0.46 | 12/5.75 | 
30 MAh Indl Charging |  |  |  |  | 
Dry Gel charging |  |  |  |  | 
OMI charging New |  |  |  |  | 
1500 KVA no3- Trac |  |  |  |  | 
Inabtech charging |  |  |  |  | 
Rack charging |  |  |  |  | 
24 MT ball mill Auto | 5.67/BDL |  |  | 10/4.25 | 
Positive expander with assy |  |  |  | 12/4.2 | 
By WBPCB
By self engaged outside agency
Stack sampling schedule for particulate matter- 25 mg / Nm3, Pb- 10 mg / Nm3
STACK SAMPLING

## Slide 29
Work zone Air monitoring schedule for SPM, RPM, SO2, NO2, Pb |  |  |  |  |  | 
Sl No | Location |  | Jan 21 |  | Jul 21 | 
1 | Auto. Grid Casting |  | 4.621,1.195,0.014,0.027,0.045 |  | 4.722,1.234,0.015,0.029,0.055 | 
2 | Auto. Pasting |  | 4.622,1.194,0.015,0.027,0.049 |  | 4.287,1.166,0.017,0.029, 0.051 | 
3 | Auto. Plate Brushing |  | 4.956,1.212,0.015,0.028,0.034 |  | 4.852,1.098,0.014,0.03,0.035 | 
4 | Auto. Assembly |  | 4.767,1.124,0.017,0.025,0.027 |  | 4.667,1.157,0.018,0.026,0.033 | 
5 | Indl. Grid Casting |  | 3.687,1.125,0.015,0.027,0.03 |  | 3.745,1.159,0.016,0.029,0.032 | 
6 | Indl. Pasting |  | 5.113,1.197,0.019,0.029,0.036 |  | 5.297,1.324,0,02,0.031,0.38 | 
7 | Indl. Rotary Shaker |  | 5.844,2.453,0.017,0.032,0.037 |  | 6.025,2.607,0.018,0.033,0.038 | 
8 | Indl. Assembly |  | 4.397,1.223,0.016,0.024,0.031 |  | 4.412,1.307, 0.017,0.026, 0.032 | 
9 | Traction Grid Casting |  | 3.875,1.023,0.014,0.029,0.034 |  | 3.924,1.101, 0.013,0.013, 0.37 | 
10 | Traction Pasting |  | 4.712,1.236,0.014,0.029,0.031 |  | 4.802,1.287,0.016,0.031,0.033 | 
11 | Traction Slurry Filling |  | 4.456,1.412,0.017,0.032,0.037 |  | 4.667,1.603,0.018,0.033,0.038 | 
12 | Traction Assembly |  | 4.321,1.339,0.012,0.024,0.027 |  | 4.485,1.412,0.013,0.026,0.032 | 
13 | Alpha Casting |  | 4.302,1.411,0.014,0.033,0.047 |  | 4.447,1.487,0.015,0.034,0.051 | 
14 | Alpha Pasting |  | 4.896,1,135,0.015,0.027,0.024 |  | 5.158,1.147,0.016,0.028,0.027 | 
15 | Alpha Reactor pot |  | 4.023,1.023,0.013,0.025,0.024 |  | 4.332,1.147,0.014,0.027,0.029 | 
12 | Traction Assembly |  | 5.237,2.362,0.012,0.32,0.033 |  | 5.698,2.204,0.014,0.034,0.039 | 
By self engaged outside agency (unit- mg/m3)
Parameter – SPM-10 mg/m3, RPM – 5 mg/m3 ,SO2 -5 mg/m3, NO2-6 mg/m3, Pb- 0.15 mg/m3

## Slide 30
 | Ambient Air Quality Monitoring schedule for PM 10, PM 2.5 ,SO2, No2 & Pb |  |  |  |  |  |  |  |  |  |  |  | 
S l No | Location | January | Feb | March | April | May | June | July | August | Sept | Oct | Nov | Dec
1 | Near Admn. Building |  |  |  | 79.43,29.01,14.52,33.88,0.82,33.41 |  |  |  |  |  |  |  | 
2 | Beside R.O. Plant of Traction Factory |  |  |  |  | 74.58,26.81,13.68,34.03,0.80,33.75 |  |  |  |  |  |  | 
3 | Near auto acid mixing area |  |  |  |  |  | 28.43,16.62,35.96,0.82, |  |  |  |  |  | 
4 | Near Traction Factory Gate |  |  |  |  |  |  | 79.95,26.26,14.49,32.72,0.82 |  |  |  |  | 
5 | Near industrial test house |  |  |  |  |  |  |  | 54.68,17.84,10.79,29.06,0.69 |  |  |  | 
6 | Near Industrial DG house |  |  |  |  |  |  |  |  | 89.16,32.05,13.62,42.14,0.87 |  |  | 
7 | Near Lihshan ball mill-traction |  |  |  |  |  |  |  |  |  | 68.73,26.91,14.72,32.73,0.66 |  | 
8 | Outside charging area of traction factory |  |  |  |  |  |  |  |  |  |  |  | 
9 | Near Auto. Test House |  |  |  |  |  |  |  |  |  |  |  | 
By self engaged outside agency
Parameter: PM10-100 µg /m3, PM2.5-60 µg /m3 , SO2- 80 µg /m3 , NO2-80 µg /m3, Pb-1 µg /m3

## Slide 31
PRODUCT RESPONSIBILITY POLICY
Ensure life cycle assessment of products in order to determine the environment impact of product
Evaluate the human & environment safety of each product through assessments of hazards associated with the raw material and their interaction with product(mixtures)

## Slide 32
Our Products are made with sustainably sourced ingredients
Lead and Lead Alloys
Sulphuric Acid
Polypropylene Co Polymer

## Slide 33
ISO 14001
Exide is ISO 14001 certified company-
Environment protection is a key element on Exide Business –
Complying all regulatory compliance
Compliance on ISO 14001 requirements
Regular monitoring on pollution control devices
Audit to find out scope of opportunities.
Looking for improvements

## Slide 34
Green Sourcing & Procurement plan
VENDOR POLICY
Establish implement and maintained QEHS system aligned to Exide business objective.
Continual improvement and sustain the efficiency of vendor manufacturing system
Comply all applicable statutory and regulatory requirements.
Deploy best practice for vendor engagement.

## Slide 35
Green Sourcing
Procuring of the environment friendly resources from well known and standard vendor.
Our vendors are also engaged in sustainability programe.
Complying all statutory and regulatory requirement.

## Slide 36
Green Sourcing

## Slide 37
Exide has been registered as a Brand Owner for disposal of MLP (Multi Layered Plastics) & other plastic waste generated due to the products as per the EPR action plan submitted to CPCB.
CPCB has granted the registration in favour of EIL
Standard Procedure of Disposal

## Slide 38
CSR Activity

## Slide 39
A School in need for
Urgent Repair
For Transformation: Activities Planned Under CSR |  |  | 
1 | 2 New Class Rooms | 6 | Water Pipe Line
2 | Class Room Furniture | 7 | Water Tank
3 | Electrification of New Class Rooms | 8 | 2 Toilets
4 | Boundary wall | 9 | Approach Road
5 | Water Purifier | 10 | School Children Health Check Up
School After CSR Project
Dariberia Lower Primary School

## Slide 40
Before
After
Before
After
Before
After
How The Transformation Happened Under CSR

## Slide 41
Activities Implemented Under CSR
New Class Rooms
Class Room Furniture
Staircase
Water Purifier
Water Pipe Line
Boundary Wall
Urinal
Toilet
Toilet

## Slide 42
Paediatric check up
Eye check up
General Health check up
Registration
Health Camp
Routine Blood Test
Health Check-up Program

## Slide 43: OPPORTUNITIES FOR IMPROVEMENT
Infrastructure
    Development of at least one alternate agency for waste Management – for continuity of operation in cases of unforeseen interruptions at current sole agency.
    A State Referral Laboratory at Haldia – Credible and quick testing services that can be utilised by industries.
Recognition
    The Pollution Control Board may recognise, reward and promote best practices of industries – some can be adopted by others.

## Slide 44
Together We Can
Together We Will
Thank you